## Slide 1: Section A.6
Statistical Process Control

## Slide 2: Definitions1
A control chart for a process consists of values plotted over time used as a graphical display to detect unusual variation in a process.
A Control Chart consists of three horizontal lines:
​A Center Line that represents the average value of the quality characteristic corresponding to the in-control state.
​An upper bound called the Upper Control Limit (UCL)
​A lower bound called the Lower Control Limit (LCL)

## Slide 3: Definitions2
Figure A6.1

## Slide 4: Definitions3
Each point on the chart represents a sample statistic which has been calculated for the sample taken at a particular time period. The sample statistic will vary depending on the type of the control chart which is being used. If the sample statistic falls above the UCL or below the LCL, this signals unusual variation in the process and the process is deemed to be "Out of Control."

## Slide 5: The Highway Control Chart
When you are driving a car and you stay in your lane, you could say that you are operating the car "in control." The white lines that define your lane are similar to the UCL and LCL. The car would be expected to move around within the lane, which would be normal process variation. Veering outside your lane might have assignable causes such as cell phone usage, children fighting in the back seat, or any number of other distractions.

## Slide 6: Definitions4
graphically display consecutive sample
means with the intent of detecting a significant change in the process mean. The three methods of constructing
deal with:
Range charts (R-Charts) graphically display consecutive sample ranges with the intent of detecting a significant change in the process variation.

## Slide 7: Definitions5
p-Charts graphically display consecutive sample proportions of defective units with the intent of detecting a significant change in the proportion of defective units which a process produces.
c-Charts graphically display the number of defects per unit. An example of a unit could be a wrist watch, a hotel room, a yard of cloth, or a mile of cable. The intent is to detect changes in the number of defects per unit which a process produces.

## Slide 8: Note1
If the same number of units are sampled at each time period (which, in general, they should be), the Center Line can also be calculated by finding the proportion of defective units in each sample and then averaging the sample proportions.

## Slide 9: Definitions6
The Upper and Lower Control Limits (UCL and LCL) represent the boundaries between variation which is random or typical for the process and variation which is non-random or unusual for the process. These values will be calculated differently depending on the type of Control Chart being used.
​Mean Chart when and are known:
​
where
​μ the process mean
​σ the process standard deviation
n the number of observations in each sample.

## Slide 10: Definitions7
​Mean Chart using

## Slide 11: Definitions8
3σ Factors for Computing Control Chart Limits
Sample Size | Mean Factor (A) | Lower Range (D3) | Upper Range (D4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  | 1.55 - 0.0015n | 0.45 + 0.001n

## Slide 12: Definitions9
​Mean Chart using sample standard deviation:
​

## Slide 13: Definitions10
p-Chart:

## Slide 14: Definitions11
c​-Chart:

## Slide 15: Note2
The wider the control limits the less likely we are to
the control limits too wide, because then we are more likely to conclude that the process is "In Control" when it is not (i.e., make a Type II Error).

## Slide 16: Definitions12
where μ is the process mean, σ is the process standard deviation, and n is the number of observations in each sample.

## Slide 17: Example A6.11
A manufacturing company uses a machine to punch out parts of a window hinge. Historically, the manufacturing process has produced hinges with a mean width of 0.45 inches with a process standard deviation of 0.022 inches. To monitor the production and to make sure the parts are acceptable for the next stage of home window assembly, a sample of three parts is taken each hour. The width of each part is then measured. As a result there are a total of eight samples with three observations in each sample. The table below contains the data for the widths of the hinges. Determine if the process is in control using an
Indicate which (if any) samples are out of control.

## Slide 18: Example A6.12
Sampling Data for Window Hinges (Inches)
Sample Number | Observation 1 | Observation 2 | Observation 3
1 | 0.42 | 0.48 | 0.46
2 | 0.44 | 0.48 | 0.45
3 | 0.44 | 0.45 | 0.41
4 | 0.47 | 0.42 | 0.46
5 | 0.53 | 0.43 | 0.42
6 | 0.47 | 0.42 | 0.45
7 | 0.44 | 0.47 | 0.50
8 | 0.48 | 0.43 | 0.44

## Slide 19: Example A6.13
Solution
Control limits need to be established and plotted on the
Typically, control limits for the
are three standard deviations
above and below the process mean for the given quality characteristic. In this problem, we have external standards to gauge our process. In particular, the process mean (0.45) and process standard deviation (0.022) are known. Thus, the control limits are determined as follows.

## Slide 20: Example A6.14
Sampling Data for Window Hinges (Inches) with Sample Mean
Sample | Observation 1 | Observation 2 | Observation 3 | Sample Mean
1 | 0.42 | 0.48 | 0.46 | 0.453
2 | 0.44 | 0.48 | 0.45 | 0.457
3 | 0.44 | 0.45 | 0.41 | 0.433
4 | 0.47 | 0.42 | 0.46 | 0.450
5 | 0.53 | 0.43 | 0.42 | 0.460
6 | 0.47 | 0.42 | 0.45 | 0.447
7 | 0.44 | 0.47 | 0.50 | 0.470
8 | 0.48 | 0.43 | 0.44 | 0.450

## Slide 21: Example A6.15

## Slide 22: Example A6.16
The mean for each sample is calculated and displayed in the table above. The sample means are plotted in the figure above along with the UCL, LCL, and center line. Note that according to the
since all of the sample means fall within the control limits, the process is in control.

## Slide 23: Definitions13

## Slide 24: Example A6.21
Using the window hinge data (reproduced below) and assuming that we do not know the mean or standard deviation of the process, construct the
for this process.

## Slide 25: Example A6.22
Sampling Data for Window Hinges (Inches)
Sample Number | Observation 1 | Observation 2 | Observation 3
1 | 0.42 | 0.48 | 0.46
2 | 0.44 | 0.48 | 0.45
3 | 0.44 | 0.45 | 0.41
4 | 0.47 | 0.42 | 0.46
5 | 0.53 | 0.43 | 0.42
6 | 0.47 | 0.42 | 0.45
7 | 0.44 | 0.47 | 0.50
8 | 0.48 | 0.43 | 0.44

## Slide 26: Example A6.23
Solution
In this example, we do not know the process standard deviation. However, we are going to use another measure of variation, the sample range, to compute the UCL and LCL. Since we do not know the true process mean, we are going to estimate that mean with the
mean of the sample means.
Before calculating the control limits for the
we need to perform some preliminary calculations. We need to calculate the mean and range for each sample. That is, the i th sample mean and range are calculated as follows.
Ri = Maximum Observation in i th Sample – Minimum Observation in i th Sample
Note that n is the number of observations in each sample.

## Slide 27: Example A6.24
The mean and range for each sample are presented in the following table.
Sampling Data for Window Hinges (Inches) with Mean and Range
Sample Number | Observation 1 | Observation 2 | Observation 3 | Mean | Range
1 | 0.42 | 0.48 | 0.46 | 0.453 | 0.06
2 | 0.44 | 0.48 | 0.45 | 0.457 | 0.04
3 | 0.44 | 0.45 | 0.41 | 0.433 | 0.04
4 | 0.47 | 0.42 | 0.46 | 0.450 | 0.05
5 | 0.53 | 0.43 | 0.42 | 0.460 | 0.11
6 | 0.47 | 0.42 | 0.45 | 0.447 | 0.05
7 | 0.44 | 0.47 | 0.50 | 0.470 | 0.06
8 | 0.48 | 0.43 | 0.44 | 0.450 | 0.05

## Slide 28: Example A6.25
Using the mean and range for each sample, we can calculate the grand mean and average range of the process. They are given by
Where m is the number of samples.
Using the data in the above table we find the grand mean and the average range to be the following.
The table below provides 3σ factors for computing control chart limits.

## Slide 29: Example A6.26
3 σ Factors for Computing Control Chart Limits
Sample Size | Mean Factor (A) | Lower Range (D3) | Upper Range (D4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  | 1.55 - 0.0015n | 0.45 + 0.001n

## Slide 30: Example A6.27
For a sample size of 3, the mean factor, A . Using a grand mean of 0.4525 and an average range of 0.0575, the control limits for the
are determined as follows.

## Slide 31: Example A6.28

## Slide 32: Example A6.29
Examining the
one can see that the process
mean is within the control limits. That is, each of the sample means fall within the control limits of the
indicating that the process is in control.

## Slide 33: Definitions14
is the mean of the sample ranges and D₃ and
D₄ are factors that can be found in the table below.

## Slide 34: Example A6.31
Using the window hinge data (reproduced below) and assuming that we do not know the mean or standard deviation of the process, construct the R chart for this process.

## Slide 35: Example A6.32
Sampling Data for Window Hinges (Inches)
Sample Number | Observation 1 | Observation 2 | Observation 3
1 | 0.42 | 0.48 | 0.46
2 | 0.44 | 0.48 | 0.45
3 | 0.44 | 0.45 | 0.41
4 | 0.47 | 0.42 | 0.46
5 | 0.53 | 0.43 | 0.42
6 | 0.47 | 0.42 | 0.45
7 | 0.44 | 0.47 | 0.50
8 | 0.48 | 0.43 | 0.44

## Slide 36: Example A6.33
Solution
In this example, we do not know the process standard deviation. However, we are going to use another measure of variation, the sample range, to compute the UCL and LCL.
Before calculating the control limits for the R chart, we need to perform some preliminary calculations. We need to calculate the range for each sample. That is, the i th sample range is calculated as follows.
Note that n is the number of observations in each sample.
The mean and range for each sample are presented in the table below.

## Slide 37: Example A6.34
Sampling Data for Window Hinges (Inches) with Mean and Range
Sample Number | Observation 1 | Observation 2 | Observation 3 | Mean | Range
1 | 0.42 | 0.48 | 0.46 | 0.453 | 0.06
2 | 0.44 | 0.48 | 0.45 | 0.457 | 0.04
3 | 0.44 | 0.45 | 0.41 | 0.433 | 0.04
4 | 0.47 | 0.42 | 0.46 | 0.450 | 0.05
5 | 0.53 | 0.43 | 0.42 | 0.460 | 0.11
6 | 0.47 | 0.42 | 0.45 | 0.447 | 0.05
7 | 0.44 | 0.47 | 0.50 | 0.470 | 0.06
8 | 0.48 | 0.43 | 0.44 | 0.450 | 0.05

## Slide 38: Example A6.35
Using the range for each sample, we can calculate the average range of the process. It is given by
where m is the number of samples.
Using the data in the table we find the average range to be the following.
The table below provides 3σ factors for computing control chart limits.

## Slide 39: Example A6.36
3σ Factors for Computing Control Chart Limits
Sample Size | Mean Factor (A) | Lower Range (D3) | Upper Range (D4)
2 | 1.880 | 0.000 | 3.267
3 | 1.023 | 0.000 | 2.574
4 | 0.729 | 0.000 | 2.282
5 | 0.577 | 0.000 | 2.114
6 | 0.483 | 0.000 | 2.004
7 | 0.419 | 0.076 | 1.924
8 | 0.373 | 0.136 | 1.864
9 | 0.337 | 0.184 | 1.816
10 | 0.308 | 0.223 | 1.777
15 | 0.223 | 0.348 | 1.652
20 | 0.180 | 0.414 | 1.586
25 | 0.153 | 0.459 | 1.541
Over 25 |  | 1.55 - 0.0015n | 0.45 + 0.001n

## Slide 40: Example A6.37
Computing the control limits for the R chart, we have

## Slide 41: Example A6.38

## Slide 42: Example A6.39
Examining the R chart, one can see that the variability is within the control limits. That is, the sample ranges fall within the control limits of the R chart, indicating that the process is in control.

## Slide 43: Example A6.4: Mean Charts Using S1
Cola Supreme has decided to use an
with an α-risk of , to determine if their 15 ounce filling machine is properly adjusted. The production manager randomly selects five cans of cola and measures the amount of cola in each can. The sampling is repeated at 15 successively selected time periods.
The results are displayed below:

## Slide 44: Example A6.4: Mean Charts Using S2
Sample Results
Sample Number | Obs. 1 | Obs. 2 | Obs. 3 | Obs. 4 | Obs. 5 | Sample Mean | Sample Standard Deviation
1 | 15.00 | 14.97 | 15.01 | 15.00 | 15.04 | 15.0040 | 0.0251
2 | 14.96 | 14.98 | 14.97 | 15.00 | 14.98 | 14.9780 | 0.0148
3 | 14.98 | 14.95 | 15.02 | 14.96 | 14.98 | 14.9780 | 0.0268
4 | 15.03 | 14.98 | 14.99 | 15.00 | 15.03 | 15.0060 | 0.0230
5 | 15.01 | 14.98 | 15.04 | 14.99 | 15.05 | 15.0140 | 0.0305
6 | 14.99 | 15.01 | 15.02 | 14.98 | 15.00 | 15.0000 | 0.0158
7 | 15.03 | 15.00 | 15.04 | 14.96 | 14.97 | 15.0000 | 0.0354
8 | 15.00 | 15.00 | 15.02 | 15.00 | 15.04 | 15.0120 | 0.0179
9 | 15.00 | 15.03 | 15.01 | 14.95 | 15.01 | 15.0000 | 0.0300
10 | 14.97 | 15.01 | 14.98 | 14.96 | 15.03 | 14.9900 | 0.0292
11 | 15.05 | 15.03 | 15.00 | 14.98 | 14.96 | 15.0040 | 0.0365
12 | 15.01 | 15.00 | 14.97 | 14.96 | 14.99 | 14.9860 | 0.0207
13 | 15.02 | 14.98 | 14.97 | 14.99 | 15.03 | 14.9980 | 0.0259
14 | 14.99 | 14.99 | 14.97 | 15.00 | 14.99 | 14.9880 | 0.0110
15 | 14.95 | 15.00 | 14.95 | 15.03 | 14.96 | 14.9780 | 0.0356

## Slide 45: Example A6.4: Mean Charts Using S3
Sample Number | Obs. 1 | Obs. 2 | Obs. 3 | Obs. 4 | Obs. 5 | Sample Mean
16 | 14.99 | 14.98 | 14.97 | 14.98 | 14.96 | 14.976
17 | 15.10 | 14.99 | 15.09 | 15.07 | 15.09 | 15.068
18 | 14.90 | 14.99 | 14.95 | 14.96 | 15.00 | 14.960

## Slide 46: Example A6.4: Mean Charts Using S4
1. What is the Center Line of the control chart?
2. ​What are the Upper and Lower Control Limits?
3. ​If the given samples are taken at the next time periods, determine if each process is "In Control" or "Out of Control"?​

## Slide 47: Example A6.4: Mean Charts Using S5
4. ​Based on the control limits established, what is the probability that the production manager will conclude that the process is "Out of Control," when the process is actually "In Control"?

## Slide 48: Example A6.4: Mean Charts Using S6
Solution
Step 1: Find the Center Line of the control chart.
To find the Center Line, calculate the average of the 15 sample means.

## Slide 49: Example A6.4: Mean Charts Using S7

## Slide 50: Example A6.4: Mean Charts Using S8
Step 2: Find the Upper and Lower Control Limits.
Since we have calculated
as 14.996, to find the
Upper Control Limit (UCL) and Lower Control Limit (LCL)
For z, the production manager wants to set the control limits such that the α-risk is , thus

## Slide 51: Example A6.4: Mean Charts Using S9
Therefore, the Upper Control Limit will be calculated as the following.
The Lower Control Limit will then be calculated as the following.

## Slide 52: Example A6.4: Mean Charts Using S10
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 16: As (i.e., the sample mean is within the control limits), the process is deemed to be "In Control."
Sample 17: As (i.e., the sample mean falls above the upper control limit), the process is deemed to be "Out of Control."
Sample 18: As (i.e., the sample mean falls below the lower control limit), the process is deemed to be "Out of Control."

## Slide 53: Example A6.4: Mean Charts Using S11

## Slide 54: Example A6.4: Mean Charts Using S12
Step 4: Find the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control".

## Slide 55: Example A6.5: p-Charts1
Miller Manufacturing has decided to use a p-Chart with 2-sigma control limits to monitor the proportion of defective circuits produced by their production process. The production manager randomly samples 100 circuits at 16 successively selected time periods and counts the number of defective circuits in the sample.
The results of the sampling are displayed below:

## Slide 56: Example A6.5: p-Charts2
Sample Data
Sample Number | # of Defects
1 | 15
2 | 10
3 | 10
4 | 11
5 | 10
6 | 9
7 | 14
8 | 11
9 | 11
10 | 14
11 | 13
12 | 14
13 | 14
14 | 10
15 | 13
16 | 13

## Slide 57: Example A6.5: p-Charts3
1. ​What is the Center Line of the control chart?
2. What are the Upper and Lower Control Limits?
3. During the next three time periods, 100 circuits are sampled in each period. In the first time period 4 defective circuits are detected, 16 are detected in the second, and 12 are detected in the third. Determine if each process is "In Control" or "Out of Control"?
4. ​Based on the control limits established, what is the probability that the production manager will conclude that the process is "Out of Control," when the process is actually "In Control"?

## Slide 58: Example A6.5: p-Charts4
Solution
Step 1: Find the Center Line of the control chart.
The Center Line is calculated as follows:

## Slide 59: Example A6.5: p-Charts5

## Slide 60: Example A6.5: p-Charts6
Step 2: Find the Upper and Lower Control Limits.
Since we have calculate
to find the Upper Control Limit (UCL) and Lower Control Limit (LCL) we need both n and z. The production manager samples 100 units at each sample period. Thus, n = 100. Since the production manager wants to set 2-sigma control limits, and z represents the number of standard deviations the control limits are set above and below the mean, z = 2.

## Slide 61: Example A6.5: p-Charts7
Therefore, the Upper Control Limit will be calculated as the following.
The Lower Control Limit will then be calculated as the following.

## Slide 62: Example A6.5: p-Charts8

## Slide 63: Example A6.5: p-Charts9
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 17: Since 0.04 falls below the Lower Control Limit, the process is deemed to be "Out of Control."
Sample 18: Since 0.16 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."
Sample 19: Since 0.12 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."

## Slide 64: Example A6.5: p-Charts10

## Slide 65: Example A6.5: p-Charts11
Step 4: Find the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control"?

## Slide 66: Example A6.5: p-Charts12

## Slide 67: Example A6.6: c-Charts1
Genuine Motors has decided to use a c-Chart to monitor the number of defects per car produced by their production process. Management would like to construct the c-Chart such that of the number of defects detected per car fall within the control limits, if the process is In Control. The production manager randomly samples one car at 16 successively selected time periods and counts the number of defects on the car.
The results of the sampling are displayed below:

## Slide 68: Example A6.6: c-Charts2
Sample Data
Sample Number | # of Defects
1 | 15
2 | 10
3 | 10
4 | 11
5 | 10
6 | 9
7 | 14
8 | 11
9 | 11
10 | 14
11 | 13
12 | 14
13 | 14
14 | 10
15 | 13
16 | 13

## Slide 69: Example A6.6: c-Charts3
1. What is the Center Line of the control chart?
2. ​What are the Upper and Lower Control Limits?
3. During the next three time periods, 4 defects are detected on the first selected car, 16 defects are detected on the second, and 12 are detected on the third. Determine if each process is "In Control" or "Out of Control"?
4. ​Based on the control limits established, what is the probability that the production manager will conclude that the process is "Out of Control," when the process is actually "In Control"?

## Slide 70: Example A6.6: c-Charts4
Solution
Step 1: Find the Center Line of the control chart.
The Center Line is calculated as follows:

## Slide 71: Example A6.6: -Charts5

## Slide 72: Example A6.6: c-Charts6
Step 2: Find the Upper and Lower Control Limits.
Since we have calculated
to find the Upper Control Limit (UCL) and Lower Control Limit (LCL) we need both n and z. The control limits must be set such that of the number of defects per unit will fall within the control limits if the process is In Control. This implies that of the observations will fall outside the control limits even if the process is In Control. Given this information, the z-value is found as follows:

## Slide 73: Example A6.6: c-Charts7
Therefore, the Upper Control Limit will be calculated as the following.
The Lower Control Limit will then be calculated as the following.

## Slide 74: Example A6.6: c-Charts8

## Slide 75: Example A6.6: c-Charts9
Step 3: For the given samples, state if the process is "In Control" or "Out of Control"
This step will be repeated for each additional sample. At each step, we must determine whether the process is "In Control" or "Out of Control."
Sample 17: Since 4 falls below the Lower Control Limit, the process is deemed to be "Out of Control."
Sample 18: Since 16 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."
Sample 19: Since 12 falls between the Upper and Lower Control Limits, the process is deemed to be "In Control."

## Slide 76: Example A6.6: c-Charts10

## Slide 77: Example A6.6: c-Charts11
Step 4: Find the probability that the production manager will conclude that the process is "Out of Control" when the process is actually "In Control"?